## Slide 1
Export of GTP-U Information in IPFIX draft-ietf-opsawg-ipfix-gtpu-00
Enabling insights in GTP forwarding plane by adding GTP-U dimensions
daniel.voyer@bell.ca
sriragop@cisco.com
thomas.graf@swisscom.com
benoit.claise@huawei.com
vyasraj@juniper.net
23 Oct 2024

## Slide 2: GTP-U @ IPFIX Draft Status since last review @ IETF119
Draft is adopted by OPSAWG
Many thanks Paul Aitken for the IPFIX doctor review.
IANA assigned IE numbers for GTP fields are available; EI 505-510.
Added a new section named ‘Operational Considerations’

## Slide 3: GTP-U @ IPFIX Data-Plane visibility is missing in GTP
GTP is the protocol used by network mobile operators for cellular networks.
Data-Plane visibility is missing in GTP-U and so unable to identify the transport performance of PDU Sessions with specific QoS within a slice or within a group of slices.

## Slide 4: GTP-U @ IPFIX IPFIX entities in context of the GTP-U (1)
gtpuFlags EI-505
  8-bit flags field defined in the GTP-U which indicates the version of GTP-U protocol, protocol type and presence of extension header, sequence number and N-PDU number in the GTP-U header.
gtpuMsgType EI-506
  8-bit message type field defined in the GTP-U which
  indicates the type of GTP-U message.
gtpuTEid EI-507
  32-bit tunnel endpoint identifier field defined in GTP-U which unambiguously identifies a tunnel endpoint in the receiving GTP-U protocol entity for a given UDP/IP endpoint..
gtpuSequenceNum EI-508
  16-bit sequence number field defined in the GTP-U. This field is interpreted based on the corresponding flag value from gtpuFlags

## Slide 5: GTP-U @ IPFIX IPFIX entities in context of the GTP-U (2)
  gtpuQFI EI-509
  8-bit QoS flow identifier field defined in PDU Session Container extension header of GTP-U. This is defined in section 5.5.3 of PDU session spec [TS.38415]. This is used to determine the QoS flow and QoS profile which are associated with the received packet.
gtpuPduType EI-510
  8-bit PDU type field defined in PDU Session Container extension header of GTP-U. This is defined in section 5.5.3 of PDU session spec [TS.38415]. This field indicates the structure of the PDU session UP frame..

## Slide 6: GTP-U @ IPFIX – Cisco IOS-XR Implementation status IPFIX Records exposed
1. gtpuFlags
  8-bit flags field defined in the GTP-U which indicates the version of GTP-U protocol, protocol type and presence of extension header, sequence number and N-PDU number in the GTP-U header.
2. gtpuMsgType
  8-bit message type field defined in the GTP-U which indicates the type of GTP-U message.
3. gtpuTEid
  32-bit tunnel endpoint identifier field defined in GTP-U which unambiguously identifies a tunnel endpoint in the receiving GTP-U protocol entity for a given UDP/IP endpoint..
4. gtpuSequenceNum
  16-bit sequence number field defined in the GTP-U. This field is interpreted based on the corresponding flag value from gtpuFlags
  5. gtpuQFI
  8-bit QoS flow identifier field defined in PDU Session Container extension header of GTP-U. This is defined in section 5.5.3 of PDU session spec [TS.38415]. This is used to determine the QoS flow and QoS profile which are associated with the received packet
6. gtpuPduType
  8-bit PDU type field defined in PDU Session Container extension header of GTP-U. This is defined in section 5.5.3 of PDU session spec [TS.38415]. This field indicates the structure of the PDU session UP frame
1
2
3
4
5
6

## Slide 7: GTP-U @ IPFIX IANA assigned IE numbers
ElementID | Name | Abstract Data Type | Data Type Semantics
505 | gtpuFlags | unsigned8 | flags
506 | gtpuMsgType | unsigned8 | identifier
507 | gtpuTEid | unsigned32 | identifier
508 | gtpuSequenceNum | unsigned16 | identifier
509 | gtpuQFI | unsigned8 | identifier
510 | gtpuPduType | unsigned8 | identifier

## Slide 8: GTP-U @ IPFIX Next Steps
Data-Plane visibility is missing in GTP.
Authors want to avoid private enterprise code points being used in GTP 5G deployments.
This draft could progress to document the use cases and will be helpful for 3GPP references also.